## Slide 1: Fault Diagnosis and Logic Debugging Using Boolean Satisfiability
ECE 7502 Class Discussion
Benjamin Melton
Thursday January 29, 2015

## Slide 2
Requirements
Specification
Architecture
Logic / Circuits
Physical Design
Fabrication
Manufacturing Test
Packaging Test
PCB Test
System Test
PCB Architecture
PCB Circuits
PCB Physical Design
PCB Fabrication
Design and Test Development
Customer
Validate
Verify
Verify
Test
Test

## Slide 3: Functional Verification
BEFORE fabrication, be sure you design it right
  Catch bugs early to prevent expensive refabrication
  Rewriting code much cheaper than respinning a chip
Work mostly done in software (maybe acceleration, FPGA, etc.)
  Can use advanced algorithms for automating verification and debug
  Circuit transformations and representations
Process
  Verification -> Errors
  Errors -> Bugs
  How to efficiently find bugs given errors?

## Slide 4: Functional Verification Challenges
Debugging modern designs is difficult
  Million+ gates
  Many error vectors to investigate
  Sequential circuits
Fixing a suspected bug might cause more errors instead.
  Headache
  Frustration
  Sleepless nights
Months of design effort (~30% of total)

## Slide 5: Paper [1] Claims
Need a way to automatically debug circuits given a set of errors
SAT, along with simple circuit insertions, can automatically locate bugs in a reasonable amount of time using a reasonable amount of resources
Can use different kinds of fault models, as well as model-free analysis.

## Slide 6: Why SAT?
Debugger performance will see immediate benefit from SAT solver advances
Conceptually simple methodology
Circuit specific characteristics reduce SAT search space

## Slide 7: Debugging With SAT
SAT – Boolean Satisfiability
  Given a Boolean expression in conjunctive normal form (CNF), what combination of input values will produce a valid output?
  Computationally difficult (NP-complete)
  Modern SAT solvers very advanced
Construct CNF from specification circuit
  Decompose complex logic gates into basic two-input gates
  Insert multiplexers in the paths between logic gates
  Duplicate circuit N times for N error vectors
  Translate circuit into CNF Boolean expression (linear time)
Attempt to reproduce circuit fault using multiplexers

## Slide 8: Debugging With SAT
[1] Smith et al, TCAD’05

## Slide 9: Multiple Fault Sites
Single or multiple faults may be present in a design
Must enforce constraint on number of faults
  Insert additional hardware into circuit to enforce constraint
  Hardware translates into the CNF for the circuit
  SAT solver enforces constraints through modified CNF
[1] Smith et al, TCAD’05

## Slide 10: Sequential Designs
Iterative Logic Array
  Model sequential circuit as several combinational stages
  Effectively unrolls the sequential circuit in time.
Applies analysis similar to the combinational case

## Slide 11: Heuristics
Several heuristics used to reduce the load on the SAT solver.
Reduce Space
  Break up vector set into chunks and process each chunk independently
  Smaller set of test vectors means smaller search space
  90% of bug candidates covered in the first couple of passes
Backtracking
  Invalidate discovered solutions
  Forces SAT solver to look for more solutions without repeating itself

## Slide 12: Heuristics
Unnecessary Branching
  If select line on a set of multiplexers is zero, the ‘1’ input to the multiplexer is irrelevant
  Remove these inputs from consideration by adding another clause to CNF
  Reduces SAT search space
Structural Information
  Investigate structural dominator lines in first pass
  Investigate all other lines in second pass
  1/5 of potential fault locations found in the first pass
  Reduces search space in second pass
  Structural dominators used extensively in [5]

## Slide 13: Heuristics
Significant speedups
  Most benchmarks see speedup
  Over 250% percent speedup for some benchmarks
[1] Smith et al, TCAD’05

## Slide 14: MaxSAT [4]
Slight change in basic SAT methodology
Given erroneous CNF and expected input and output clauses, find the maximum number of clauses that can be satisfied.
  CNF with expected input and output clauses is unsatisfiable
  Remaining unsatisfiable clauses (gates) are candidate bugs
Can indicate invalid gate type placement
Vs SAT
  4.5x improvement in performance
  80% less resource consumption

## Slide 15: Interpolation [3] & Dominance [5]
Reduce problem size
Interpolation
  Interpolants reduce storage of simulation
  Breaks problem into smaller chunks
  57% reduction in memory consumption
  Comes at a cost of 2% increase in number of error locations reported
Structural Dominance
  Find nonsolutions, blocks guaranteed to be bug free
  Use structural dominance to infer other nonsolutions
  Nonsolutions reduce SAT search space
[5] Mangassarian et al, TCAD’14

## Slide 16: Conclusion
Need to effectively debug large designs
SAT methodology effectively locates bugs within a design.
Improve speed
  A slightly different approach, MaxSAT, reduces the time and space required.
  Structural dominance reduces SAT calls and improves the speed of each call
Interpolation significantly reduces space used
All techniques benefit directly from improvements in SAT solver technology

## Slide 17: Discussion questions
The first heuristic uses multiple passes of vector subsets to reduce the solution space. Is there any difference between this and iteratively eliminating passing vectors after performing circuit correction?
Any other ways to improve performance?
Is model-free analysis guaranteed to find all faults given sufficient vector coverage? Insufficient coverage?
Page 12, paragraph 1, how does the data suggest that model-based outperforms model-free?
How could this methodology be applied to post-silicon verification and test?

## Slide 18: Papers
[1] Smith, A.; Veneris, A.; Fahim Ali, M.; Viglas, A., "Fault diagnosis and logic debugging using Boolean satisfiability," Computer-Aided Design of Integrated Circuits and Systems, IEEE Transactions on , vol.24, no.10, pp.1606,1621, Oct. 2005
[2] Safarpour, S.; Mangassarian, H.; Veneris, A.; Liffiton, Mark H.; Sakallah, K.A., "Improved Design Debugging Using Maximum Satisfiability," Formal Methods in Computer Aided Design, 2007. FMCAD '07 , vol., no., pp.13,19, 11-14 Nov. 2007
[3] Keng, B.; Veneris, A., "Scaling VLSI design debugging with interpolation," Formal Methods in Computer-Aided Design, 2009. FMCAD 2009 , vol., no., pp.144,151, 15-18 Nov. 2009
[4] Yibin Chen; Safarpour, S.; Marques-Silva, J.; Veneris, A., "Automated Design Debugging With Maximum Satisfiability," Computer-Aided Design of Integrated Circuits and Systems, IEEE Transactions on , vol.29, no.11, pp.1804,1817, Nov. 2010
[5] Mangassarian, H.; Bao Le; Veneris, A., "Debugging RTL Using Structural Dominance," Computer-Aided Design of Integrated Circuits and Systems, IEEE Transactions on , vol.33, no.1, pp.153,166, Jan. 2014

## Slide 19: Paper Map (e.g.)
[1] Smith, A.; …"Fault diagnosis and logic debugging using Boolean …," TCAD’05.
[2] Safarpour, S.; …"Improved Design Debugging Using Maximum …," FMCAD'07.
[3] Keng, B.; …"Scaling VLSI design debugging with interpolation," FMCAD’09.
[4] Yibin Chen; …"Automated Design Debugging With Maximum …," TCAD’10.
[5] Mangassarian, H.; …"Debugging RTL Using Structural Dominance,“ TCAD’14.
[1] First paper on topic of using SAT for automated debugging.
[2] MaxSAT based debugging improves performance vs SAT.
[4] Additional optimizations to MaxSAT debugging algorithm.
[3] Partition circuit into smaller sub-circuits to reduce complexity.
Slightly different algorithm
Practical applications necessitate lower resource footprint
[4] builds on [2]
[5] Most recent work on optimization of SAT debugging.
Use structural dominance

## Slide 20: Glossary
Model-free: No fault model is used. Does not restrict the failure modes of a circuit.
Model-based: Assumes a fault model. Reduces SAT search space at the expense of
Structural Dominator: Any line a where all paths from some other line a’ to a primary output must pass through a.
CNF: Conjunctive normal form. Similar to product-of-sums representation.